## Slide 1: Infection Control for Dental Healthcare Professionals

## Slide 2
Eve Cuny, MS
Executive Associate Dean and Professor
University of the Pacific
Dugoni School of Dentistry

## Slide 3: Infection Prevention and Control Guidelines
CDC
  Interim infection prevention guidelines for COVID-19
  Core practices for infection prevention and control
  Transmission-based precautions
  Additional guidelines exist in areas such as
    Sterilization and disinfection
    Hand hygiene
    Healthcare personnel (vaccine, post-exposure management, etc.)
    Healthcare worker vaccinations
    Disease-specific guidelines (TB, hepatitis B, HIV, etc)
  Summary of Infection Prevention Practices in Dental Settings (not a guideline)
mmary of Infection Prevention Practices in Dental Settings

## Slide 4: Additional Regulations and Guidelines
OSHA
  Bloodborne Pathogens Rule
  Hazard Communication
  Respiratory Protection Program
  Injury and Illness Prevention
State Boards of Dentistry
  Infection control
EPA
  Surface disinfectant registration
State Health Departments
  Regulated Medical Waste
AAMI/ANSI
  Sterilization
FDA
  Manufacturer labeling, and instructions for use
  High level disinfectant registration
Notes: In addition to accreditation/certification of outpatient clinics, eg; AAAHC, CMS, etc.

## Slide 5: Precautions to prevent transmission in healthcare
Standard
  Used in the care of all patients as foundational precautions
Transmission-based
  in addition to standard precautions to interrupt the spread of certain pathogens
  Contact
  Droplet
  Airborne
    Currently under review by HICPAC
      Possibly combining droplet and airborne
      May reduce emphasis on AGP’s since patients are always expelling aerosols regardless of the procedure
    Nothing has been finalized—stay tuned

## Slide 6: Vaccinations
Hepatitis B
Measles/Mumps/Rubella
Varicella
Tdap
Polio
Influenza
COVID-19
Other vaccines recommended for locations where diseases not common in US are prevalent (e.g., yellow fever, typhoid), or during outbreaks.

## Slide 7: Standard Precautions
Standard Precautions are a set of infection control practices that healthcare personnel use to reduce transmission of microorganisms in healthcare settings.
Standard Precautions protect both healthcare personnel and patients from contact with infectious agents.

## Slide 8: Standard precautions
Elements include:
  Hand hygiene.
  Using personal protective equipment (PPE).
  Respiratory hygiene/cough etiquette.
  Sharps safety, including engineering and work practice controls.
  Safe injection practices.
  Sterilization and disinfection of instruments and devices.
  Cleaning and disinfecting environmental surfaces.

## Slide 9: Personal protective equipment
Preventing contact with blood and body fluids

## Slide 10: Personal Protective Equipment (PPE)
Worn whenever there is a potential for:
  Contact with patients’ body fluids
    Blood
    Saliva
    Wound exudate

## Slide 11: Cal/OSHA requirements
Employer must provide appropriate PPE
1
Employer must replace PPE when needed
2
Employer must ensure its use by employees
3

## Slide 12: Masks and Protective Eyewear
Surgical facemasks in combination with face shields or protective eyewear
Change masks between patients
Clean and disinfect reusable face/eye protection between patients

## Slide 13
Protective Eyewear
Glasses with solid side shield
Goggles
Chin-length face shield
Required in situations where spray or spatter of patient body fluids may be possible (e.g.; handpiece use, air/water syringe, ultrasonic scaler)
Evidence indicates eye protection is effective in preventing the transmission of SARS-CoV-2

## Slide 14: Face Shields—the protector of the protection
During testing of an influenza-laden cough aerosol with a volume median diameter (VMD) of 8.5 μm, wearing a face shield reduced the inhalational exposure of the worker by 96% in the period immediately after a cough. The face shield also reduced the surface contamination of a respirator by 97%
https://oeh.tandfonline.com/doi/full/10.1080/15459624.2013.877591
Notes: This ability to protect our masks and respirators becomes even more important as we move into talking about reuse and decontamination strategies.
A face shield that extends from your forehead to just below your chin will help protect your eyes as well as your mask
Face shields are being 3d printed at many places across the country, and can also be easily made with craft items you can probably source. See the information at the end of the webinar in the resources section

## Slide 15: Face Mask
To protect mucous membranes from splash, spray and spatter
Changed between patients or more often if soiled or wet
Worn in combination with eye protection
Does not provide respiratory protection against aerosolized particles

## Slide 16: Attire
Reusable or disposable gown or lab coat
Under same conditions as other PPE and for disinfection, sterilization and housekeeping procedures involving germicides or contamination
Changed daily or between patients if moist or soiled
Remove before leaving patient care or laboratory areas
Discarded or laundered as per OSHA

## Slide 17: Contaminated Laundry
“Laundry which has been soiled with blood or other potentially infectious materials or may contain sharps.”
      OSHA Bloodborne Pathogens Rule

## Slide 18: OSHA Laundry Requirement
The employer shall clean, launder, and dispose of personal protective equipment at no cost to the employee
Placed in containers that are labeled or color-coded
Transported in containers that are labeled or color-coded
May be done onsite (by trained employees) or by a professional service (ensure the use of Standard Precautions)

## Slide 19: Exam Gloves
For contact with mucous membranes, blood, OPIM
Appropriate for most dental procedures
Sterile gloves for surgical procedures

## Slide 20: Heavy-duty utility Gloves
Heavy-duty utility gloves
  When handling contaminated sharp instruments and devices during reprocessing

## Slide 21: Hand Hygiene – Soap and Water
At the start and end of each workday
If hands are contaminated or visibly soiled
Before placing and after removing gloves (may use ABHR in place of soap and water if no visible soil)

## Slide 22: Alcohol-based Hand Sanitizers
Alternative to soap and water
For hands free of debris
Good antimicrobial
Not a cleaning agent

## Slide 23: Patient Care Restrictions
Refrain from direct patient care and handling patient care equipment if:
  Weeping dermatitis
  Exudative lesions

## Slide 24: Needle and Sharp Safety
Accident prevention and exposure follow-up

## Slide 25: Safety Devices (ESIP)
Required if available
  Not limited to safety needles/syringes
  Need to be sought out and evaluated
Exceptions
  Not available on the market
  Not safer than traditional devices
  Interferes with delivery of patient care

## Slide 26: Sharps Containers
Disposable needles, syringes, scalpels, ends of orthodontic wires, broken glass, etc.
Discard as soon as feasible after use
Close as possible to point of use
Do not bend or break needles for disposal

## Slide 27: Evaluate Work Practices
Seek safer ways of doing things

## Slide 28: Ergonomics
Designing and arranging things people use so that the people and things interact most efficiently and safely

## Slide 29: Ergonomics – Risky Behaviors

## Slide 30: Instrument transfers
Develop a system, train everyone and use the same method consistently.

## Slide 31: One-handed recapping or recapping device

## Slide 32: Exposure Incident
Percutaneous injury
Splash to mucous membranes
Contact with nonintact skin

## Slide 33: Post-exposure Management
Prompt reporting of injuries
Interview of patient
Testing of patient and exposed worker
Referral for medical counseling
Written report documenting details of incident, including whether or not a safety device was involved

## Slide 34: Clinical Surface Disinfection

## Slide 35: Why worry about surface disinfection?
HIV
Hours
HSV
Hours
Rhinovirus
14 Hours
Staph
5 Days
HBV
7 Days
TB
6 to 8 Months
HCV
6 Weeks

## Slide 36: Environmental Surface Disinfection

## Slide 37: Resistance to Chemical Germicides
Bacterial spores
Mycobacterium
Nonlipid or small virus
Fungi
Vegetative bacteria
Lipid or medium size virus

## Slide 38: Classification of disinfectants
* Some high-level disinfectants will kill spores with prolonged exposure times (3–12 hours); these are called high level disinfectants/sterilants
Low-level | Kill most vegetative bacteria, some fungi, and some viruses in a practical period of time (≤10 minutes). Do not kill mycobacteria.
Intermediate-level | Kill mycobacteria, vegetative bacteria, most viruses, and most fungi but do not necessarily kill bacterial spores.
High-level* | Will kill all microorganisms except large numbers of bacterial spores.

## Slide 39: Housekeeping Surfaces

## Slide 40: Clinical Contact Surfaces

## Slide 41: Equipment Barriers
Use surface barriers to protect clinical contact surfaces, particularly those that are difficult to clean
Change between patients
Disinfect underlying surface if it is inadvertently contaminated when removing barrier

## Slide 42: Spray – Wipe - Spray
Spray on cleaner (or cleaner disinfectant)
Wipe to clean
Spray on disinfectant and then WAIT – follow label directions for contact time

## Slide 43: Wipe – Throw - Wipe
Wipe on cleaner (or cleaner/disinfectant) with premoistened towelette
Throw away wipe (multiple surfaces will require multiple towelettes)
Wipe with fresh towelette(s) and WAIT – allow surface to remain wet for time indicated on the label

## Slide 44: Effective Decontamination
The most effective method to remove contamination is wipe – toss – wipe
Contamination can be spread from surface-to-surface by using one wipe to apply disinfectant to multiple surfaces

## Slide 45: Instrument Processing
Transporting, cleaning, sterilizing and storing

## Slide 46: The instrument processing cycle

## Slide 47: Spaulding's Classification of Instruments
Category | Definition | Reprocessing | Examples
Critical | Penetrate soft tissue or bone | Sterilization | Surgical instruments, periodontal scalers
Semicritical | Contact mucous membranes or non-intact skin | Sterilization or high-level disinfection | dental mouth mirrors, amalgam condenser, Handpieces and handpiece components
Noncritical | Contact intact (unbroken) skin | low- to intermediate-level disinfection | X-ray head/cone, facebow

## Slide 48: Sterilization of Instruments
Critical and semicritical instruments
  Cleaned
  Heat sterilize
  High level disinfect or sterilize using chemical germicides only if item cannot be heat sterilized
  Discard if disposable
Heat sterilize all high-speed handpieces, low-speed handpieces, rotary components and all other attachments (e.g.: reusable air/water syringe tips, ultrasonic scaler tips, etc.)

## Slide 49: Heat-Based Sterilization
Steam under pressure (autoclaving)
  Gravity displacement
  Dynamic air removal
    Steam-flush pressure pulse
    prevacuum
Dry heat
  Static air (convection, oven-type)
  Forced air (rapid heat transfer)
Unsaturated chemical vapor
  Proprietary formula of alcohol/formaldehyde

## Slide 50: Comparison of Gravity and Dynamic Air Removal Autoclaves
 | Gravity | Dynamic Air Removal
Mechanism | Steam injects into chamber, forms a stratified layer, and its mass displaces air via drain vent | Cycles of steam flush, pressure pulse removes air from chamber and packaged materials
Temperature | 1210 C | 132 – 1350 C
Sterilization time | ~ 30 mins | 3-5 mins
Drying time | 30 mins | 30 mins
Type of instrument sets | Unwrapped and lightly wrapped | All types, including devices with lumens

## Slide 51: Consider Work Flow When Planning

## Slide 52: Proper Work Flow Prevents Errors

## Slide 53: Cleaning Before Sterilization -- Ultrasonic

## Slide 54: Hand Scrubbing
For instruments that cannot be submerged in liquids
For instruments with debris that remains after mechanical cleaning
Instruments with lumens may require cleaning with a brush

## Slide 55: Presoak/Prespray
May be used to hold instruments until cleaning can be done
Some solutions may help loosen stubborn debris
Not required prior to cleaning
  Useful if instruments cannot be cleaned immediately and for heavily soiled items, such as surgical instruments
Enzyme Spray

## Slide 56: Drying Instruments
Dry instruments carefully
Remove debris that was not cleaned mechanically
Wear heavy-duty gloves to process instruments

## Slide 57: Packaging Instruments
Carefully place instruments in pouch or wrap
Use materials compatible with type of sterilizer

## Slide 58: Loading the Sterilizer
Light items on top
Heavy items on the bottom
Peel pouches (on edge)
Perforated wrapped trays (flat)
Solid wrapped trays (on edge)

## Slide 59: Chemical Indicators
Measure key parameters of the sterilization process (e.g. time, temperature)
Visual change when the desired parameter has been achieved
Single parameter indicators, multi-parameter indicators and integrators
  Recommended by CDC and AAMI
  One inside each pack and one on the outside if the inside one is not visible

## Slide 60: Biologic Monitoring (Spore Test)
Contain bacterial spores resistant to heat sterilization
Highest level of confirmation for sterilization
Weekly spore testing recommended (requirements vary by state)

## Slide 61: Issues in Sterilization
CDC Health Advisory October 2015
CDC/FDA Health Update about the Immediate Need for Healthcare Facilities to Review Procedures for Cleaning, Disinfecting, and Sterilizing Reusable Medical Devices
Numerous reports of breaches in reprocessing of instruments and devices in health care settings
  Leading to notification of thousands of patients regarding potential exposure to bloodborne diseases

## Slide 62: Liquid Chemical Sterilant/Disinfectants
Heat tolerant or disposable alternative available for most items
The use of high-level disinfectants is discouraged by CDC

## Slide 63: Use of High-Level Disinfectants
Ventilation
  OSHA recommendations/best practices
Disposal
  May be hazardous waste
Risks
  Skin irritation
  Asthma potential
Items are not packaged and there is no process validation, such as chemical indicators and spore tests

## Slide 64: What if I open a sterile pack but don’t use the instruments?
All instruments opened in the operating or procedure room should be considered contaminated whether or not they have been used.
Rationale: Scrubbed persons might touch instruments without being aware of it. Used instruments also might come in contact with other instruments.
AAMI/ANSI

## Slide 65: How can I protect instruments from damage?
place instruments into their respective containers, tray, instrument pans for transport
have a process in place to identify instruments in need of repair/maintenance and removal from service (e.g; a tag)
protect delicate instruments from damage (cassettes)
segregate reusable sharp instruments inside the container
place heavy instrumentation on the bottom and lighter, delicate instruments on top.

## Slide 66: If sterilization is good—sterilization combined with disinfection is better – right?
Instruments and devices should not be treated with any additional chemical (e.g., alcohol, disinfectant wipes) unless such treatment is specifically recommended in the manufacturer’s written IFU.
AAMI/ANSI

## Slide 67: Single-use Items
Used for one patient and discarded appropriately
  Disposable prophy angles, prophy cups and brushes, plastic high speed evacuator tips, saliva ejectors, disposable a/w syringe tips, gloves

## Slide 68: Dental Waterline Contamination

## Slide 69: How do waterlines become contaminated?
Biofilm forms on the inner lining of tubes delivering water to dental devices
  Biofilm provides a nutrient-rich environment for the colonization of certain bacteria
  Over time, if untreated, the biofilm becomes laden with enough bacteria to result in water that would not be considered suitable for drinking
  Studies have shown untreated lines produce 100,000 - >1,000,000 cfu/mL of bacteria*
  *Szymanska J, Sitkowska J.Bacterial contamination of dental unit waterlines. Environ Monit Assess. 2013 May; 185(5): 3603–3611.

## Slide 70: Dental Waterline Management
CDC guidelines establish 500 CFU of heterotrophic bacteria as the goal for maintaining water quality
Use products designed to control biofilm in water lines
Do not use surface disinfectants or other products that have not been tested as safe and effective for water lines
Test water for heterotrophic bacteria on a regular basis and retreat with initial treatment if bacteria is increasing
Initial treatment with a product to remove biofilm is usually needed

## Slide 71: Mycobacterium abcessus infections among children
2015
  20 children admitted to local hospitals near Atlanta, GA, USA
  All children had severe illness, 17 required surgery
  The CDC determined the source of infections were from dental treatment water in a single clinic with untreated waterlines
    All children had pulpotomies performed in the days before onset of illness
2016
  A second cluster of infected children emerged in California, USA
  At least 58 children became ill after receiving pulpotomies at a dental clinic
  Health officials linked infections to contamination of dental treatment water with Mycobacterium abcessus

## Slide 72: Independent reservoirs
Tablets or liquids added to treatment water
Follow instructions for use provided by the treatment product manufacturer
Do not use surface disinfectants
Diluted bleach has been used but may cause damage to internal components of dental unit
Water testing may be needed to ensure water quality is maintained

## Slide 73: CDC Guidelines 2003 Dental Unit Waterlines and Water Quality
For non-surgical treatment use water that meets EPA drinking water standards (< 500 CFU/mL of HPC bacteria)
Consult with dental unit manufacturer for appropriate methods to maintain dental water quality
Follow manufacturer recommendations for monitoring water quality
In July 2023 a working group was formed within HICPAC to develop guidelines for dental waterline biofilm control.

## Slide 74: Transmission-based Precautions
Modes of transmission for which standard precautions may not provide enough protection

## Slide 75: 2007 Guideline for Isolation Precautions: Preventing Transmission of Infectious Agents in Healthcare Settings
CDC: Jane D. Siegel, MD; Emily Rhinehart, RN MPH CIC; Marguerite Jackson, PhD; Linda Chiarello, RN MS; the Healthcare Infection Control Practices Advisory Committee

## Slide 76: Transmission-based precautions
For patients who are known or suspected to be infected or colonized with infectious agents, including certain epidemiologically important pathogens, which require additional control measures to effectively prevent transmission.
Implemented in addition to standard precautions

## Slide 77: Three principal routes of transmission in healthcare settings requiring precautions beyond standard precautions
Contact
Droplet
Airborne

## Slide 78: Managing patients requiring airborne precautions
Always screen patients for respiratory symptoms, and whether they are confirmed or under investigation for infection with airborne transmissible disease
Delay routine dental treatment
If they present to the office, place a mask on patients with a cough and reschedule appointment
Emergency care
  Determine if treatment can be delayed with providing supportive care (pain medication, antibiotics, home care)
  If treatment must be provided, refer to a facility equipped for airborne precautions

## Slide 79: Thank you